CRTC INDUSTRY STEERING COMMITTEE

TIF REPORT

Date Submitted: 	26 February 2003

WORKING GROUP:  Canadian Steering Committee on Numbering (CSCN)

REPORT #:	CSCN TIF Report 30				File ID: CNRE030A.doc

REPORT TITLE: CSCN TIF 46 Report re: International Mobile Station Identity (IMSI) Guidelines

OUTCOME: 			Consensus

RELATED TASK(s) #:	None

BACKGROUND:

On 25 September 2001 the Canadian Radio-television and Telecommunications Commission (CRTC) released Decision CRTC 2001-605, “Re:  Canadian Numbering Administration Consortium – Application to transfer administrative responsibilities to the Canadian Numbering Administration (CNA)”.  In this Decision, the CRTC accepted the transfer from Industry Canada to the CRTC of regulatory responsibility for International Mobile Station Identifiers (IMSIs) and System Identifier Codes (SIDs).  In addition, the CRTC assigned the administrative responsibility for the assignment of IMSIs and SIDs to the CNA.  The Decision states:

The CNA will assign these resources as described in the applicable guidelines until such time as the Commission has received, reviewed and approved new versions of these guidelines.

At CSCN 59, the CNA noted that, based on the quotation cited above, the CSCN should create guidelines for the administration of IMSIs and SIDs for approval by the Commission.

On February 6, 2002, at CSCN 60, TIF 46 relating to the development of guidelines for the administration of International Mobile Station Identifier (IMSI) and System Identifier (SID) codes was accepted by the CSCN.  Since that time, the TIF 46 Task Force has created a set of guidelines for the administration of IMSIs in Canada, which were discussed and approved by the CSCN on February 26, 2003.

The TIF 46 Task Force will continue to work on developing guidelines for the administration of SIDs in Canada.

RECOMMENDATIONS:

The CSCN recommends that CISC and CRTC approve the Canadian International Mobile Station Identity (IMSI) Assignment Guidelines developed by the CSCN for use in Canada.

A copy of the proposed Canadian International Mobile Station Identity (IMSI) Assignment Guidelines is attached to this TIF Report.

February 17, 2003

Canadian

International Mobile Station Identity (IMSI)

Assignment Guidelines

Developed by:

The Canadian Steering Committee on Numbering (CSCN)

Approved by CRTC:

TABLE OF CONTENTS

Page

1.0	INTRODUCTION	1

2.0	PURPOSE AND SCOPE	1

3.0	REFERENCES	2

4.0	IMSI FORMAT AND FUNCTION	2

5.0	ASSUMPTIONS AND CONSTRAINTS	4

6.0	ASSIGNMENT PRINCIPLES	4

7.0	CRITERIA FOR HNI ASSIGNMENT	6

8.0	RESPONSIBILITIES OF HNI APPLICANTS AND ASSIGNEES	6

9.0	RESPONSIBILITIES OF THE IMSI ADMINISTRATOR	7

10.0	HNI RETURN AND RECLAMATION PROCEDURES	9

11.0	IMSI RESOURCE CONSERVATION AND ASSIGNMENT AUDITS	9

12.0	MCC RELIEF PLANNING	10

13.0	MAINTENANCE OF GUIDELINES	10

14.0	APPEALS PROCESS	10

15.0	GLOSSARY	11

APPENDIX 1 - Temporary Accommodation for GSM-Based Wireless Networks	13

FORMS

### 1.0	INTRODUCTION

The Canadian Steering Committer on Numbering (CSCN) developed these Guidelines for use in Canada.  They become effective upon review by the CRTC Interconnection Steering Committee (CISC) and approval by the Canadian Radio-television and Telecommunications Commission (CRTC).

In Canada, the Canadian Numbering Administrator (CNA) undertakes the primary administrative functions for all International Mobile Station Identity (IMSI) resources.  The CNA administers IMSI resources in accordance with Guidelines developed by the CSCN and approved by the CRTC.  The administration of IMSIs in Canada is conducted under the regulatory authority of the CRTC.

### 2.0	PURPOSE AND SCOPE

This document contains the Guidelines for the assignment and use of IMSIs for Wireless Service Providers (WSP) and Wireless Competitive Local Exchange Carriers (WCLEC) in Canada.

2.1	For the purpose of these Guidelines, a WSP or WCLEC is defined as a Canadian entity authorized by Industry Canada pursuant to the Radiocommunication Act to provide two-way common carrier wireless mobility communications service to the public.  Examples of WSPs and WCLECs include Cellular, Personal Communications Services (PCS), Enhanced Specialized Mobile Radio (ESMR), and Mobile Satellite Services (MSS).

2.2	These Guidelines pertain to the entire Canadian IMSI resource.  The IMSI administrator administers only the Home Network Identity (HNI) segment of the IMSI.  The HNI uniquely identifies the home wireless network of a WSP or WCLEC subscriber and contains the Mobile Country Code (MCC) and the Mobile Network Code (MNC).  The remaining segment of the IMSI, the Mobile Station Identification Number (MSIN), is directly administered by the wireless network licensee to which the HNI is assigned.

2.3	These Guidelines apply throughout Canada and do not supersede the regulations, procedures or requirements of the CRTC or any other appropriate legal or regulatory authority.

2.4	These Guidelines are based on the content of ITU-T Recommendation E.212, Identification Plan for Land Mobile Stations.

### 3.0	REFERENCES

3.1	ITU-T Recommendation E.212, Identification Plan for Land Mobile Stations.

A copy of ITU-T Recommendation E.212 can be viewed at:  http://ecs.itu.ch/cgi-bin/run/dms-ebookshop?choice=status&customerid.  Some charges may be incurred for accessing portions of the ITU website.  No part of the Recommendation can be copied without the express permission of the ITU.

### 4.0	IMSI FORMAT AND FUNCTION

4.1	The IMSI format and function are based on ITU-T Recommendation E.212.

4.2	Each IMSI uniquely identifies the mobile station, the home wireless network of the mobile station, and the home country of the home wireless network.

4.3	Wireless networks which conform to ITU-T Recommendation E.212 use IMSIs for:

- determination of a mobile station's home wireless network,

- mobile station identification when information about a mobile station is to be exchanged between visited and home wireless networks, including subscription and billing information needed to enable charging of visiting mobile stations,

- mobile station identification on the radio control path for registering a mobile station in a visited wireless network,

- mobile station identification for signaling on the radio control path, and

- subscription management, i.e. retrieving, providing, changing, and updating subscription data for a mobile station.

4.4	The format of the IMSI in North America is:

4.5	The IMSI format in Canada is a fixed 15-digit length -- the maximum allowable by Recommendation E.212.  Each IMSI contains an MCC, an MNC, and an MSIN.  The MCC and MNC combine to form the HNI, which is the segment of the IMSI directly administered by the IMSI administrator.  The MNC and MSIN together form the NMSI.  MSINs are administered directly by the wireless network licensee to which the HNI is assigned.

4.6	The function of the MCC is to identify the domiciliary country of a mobile station.  By analyzing the MCC, a foreign visited wireless network can determine the country from which the mobile station originated and in which its home wireless network resides.

According to ITU-T Recommendation E.212, an MCC is three digits in length and is in the format NXX, where N equals any of the decimal digits 2-9, and X equals any of the decimal digits 0-9.  MCCs are assigned by the ITU in response to formal requests from recognized national administrators of ITU-member countries.  In Canada, the recognized national administrator for ITU resources is Industry Canada.  The MCC currently assigned to Canada is 302.

4.7	The function of the MNC is to identify the home wireless network, within the country associated with the MCC, of the visiting mobile station.  The visited wireless network uses the MCC-MNC combination to identify and query the home wireless network of the visiting mobile station that is requesting service.

MNCs are three digits in length and in the format XXX, where X equals any of the decimal digits 0-9.  The 3-digit maximum is necessary so that, when combined with the 3-digit MCC, the visited wireless network need not analyze more than 6 digits to determine the home wireless network of the visiting mobile station -- another ITU-T Recommendation E.212 requirement.  This format provides one thousand MNCs (000-999) for each MCC.  (See Appendix 1 for “temporary” GSM - based limitations on MNC assignments.)

4.8	The function of the MSIN is to uniquely identify a mobile station within its home wireless network.

MSINs in Canada are nine digits in length and in the format XXXXXXXXX, where X equals any of the decimal digits 0-9.  ITU-T Recommendation E.212 limits IMSI length to a fifteen-digit maximum.  Since the Canadian IMSI format includes a six-digit HNI, a nine-digit MSIN is the maximum allowable.  The nine-digit format provides one billion MSINs per MNC or wireless network.

4.9	The NMSI contains the MNC followed by the MSIN and is a fixed twelve-digit length in Canada.  It is the national portion of the IMSI, i.e. excluding the MCC. Its length and format are determined nationally within the constraints of ITU-T Recommendation E.212.

4.10	The HNI contains the MCC followed by the MNC and is a fixed 6-digit length.  The HNI uniquely identifies the home wireless service provider.  The HNI format accommodates the potential for obtaining additional mobile country code assignments in the event of the exhaust of the MNC resource.

### 5.0	ASSUMPTIONS AND CONSTRAINTS

These Guidelines are based on the following assumptions and constraints:

  - These Guidelines should provide the greatest latitude to those providing WSP or WCLEC services while permitting the effective and efficient management of a finite resource.

  - The function of the IMSI administrator will be performed by the CNA.

  - The Guidelines for IMSI assignment for WSPs or WCLECs as set forth in this document remain in effect till there is regulatory approval to change them.

  - These Guidelines do not describe the method by which IMSIs are transmitted between and processed by networks.  Network interworking arrangements are contained in other standards, documents, or business agreements.

### 6.0	ASSIGNMENT PRINCIPLES

The following assignment principles will apply to the assignment of HNIs by the IMSI administrator and the use of IMSIs by assignees:

  - HNIs are to be assigned and used only for WSPs or WCLECs, in accordance with these Guidelines.

  - On receipt of a valid application, the IMSI administrator will assign an initial HNI for each WSP or WCLEC.  In exceptional circumstances, in order to accommodate certain technological or operational constraints, e.g., where separate facility-based wireless networks are provided by a WSP or WCLEC, the IMSI administrator can assign an additional HNI.  In the event that a WSP or WCLEC submits an application for a third HNI, the IMSI administrator shall consult with CRTC staff before making an assignment decision.

  - The 6-digit HNI, as part of the 15-digit IMSI, is to be assigned so as to uniquely identify the home wireless network of the WSP and WCLEC service user.

  - MSINs are assigned by wireless network operators to their subscribed mobile stations.  An individual IMSI may only be assigned to a single mobile station; however, more than one IMSI may be assigned to a mobile station.

  - IMSIs and HNIs shall be assigned to permit the most effective and efficient use of a finite resource in order to defer, as long as practical, the need to request additional MCC resources.

  - IMSIs are a public resource.  The assignment of any portion of an IMSI (i.e., HNI, MSIN) does not imply ownership of the resource by either the entity to which it is assigned or by the entity performing the administrative function.

  - Should an assignee transfer control of its WSP or WCLEC licenses through acquisition or merger to another licensee, then the use of the assigned HNI is transferable to that licensee.

  - The IMSI administrator will:

- Assign HNIs in a fair, timely and impartial manner to any applicant that meets the criteria for assignment contained in these Guidelines.

- Assign HNIs on a first come, first served basis from the available pool of unassigned HNIs.

- Assign HNIs for wireless carriers authorized by Industry Canada to provide service on an experimental basis.  In the event the wireless carrier is subsequently authorized to provide service on a regular basis, the assignee may retain the same HNIs assigned under the experimental operation.

- Make all assignments based on the procedures in these Guidelines.

- Treat sensitive information received from applicants as proprietary and confidential.

  - Information that is requested of applicants in support of an HNI application shall be uniform and kept to a minimum.

  - Assigned HNIs should be deployed as soon as possible, but no later than twelve months after initial assignment.  If the assignee can demonstrate that an assigned HNI has not been deployed solely due to delays beyond its control, the time period can be extended for up to 90 days.  At the discretion of the administrator, up to three additional 90-day extensions may be granted.

  - An entity which is denied an HNI assignment or extension under these Guidelines has the right to appeal that decision in writing to the CRTC with a copy provided to the IMSI administrator.

  - An HNI recovered or returned to the administrator for reassignment will be aged for a period of not less than one year, from the date of return to the HNI pool, before reassignment.

  - Applicants for HNIs must comply with all applicable Canadian regulatory requirements in regards to the provisioning of WSP or WCLEC services.

### 7.0	CRITERIA FOR HNI ASSIGNMENT

The assignment criteria in the following paragraphs should be considered by a potential HNI applicant before submitting an HNI application and will be used by the IMSI administrator in reviewing and processing an HNI application:

  - The HNI applicant must be licensed by Industry Canada for the spectrum utilized by its wireless network(s) and must have provided evidence or certification to the IMSI administrator.

7.2	The applicant/assignee of an HNI must be authorized by the appropriate Canadian regulatory authority to operate in the area in which it intends to provide WSP or WCLEC service and, if required, it must provide evidence of this authorization.

7.3	An HNI will only be assigned by the IMSI administrator upon receipt and approval of a completed Form A – Home Network Identity (HNI) Application.

7.4	A second HNI may be assigned to an applicant in order to accommodate certain technological or operational constraints.  (See section 6.2.)  The applicant must provide a description of the technological or operational constraints and an explanation of how the assignment of an additional HNI resource will resolve the described technological or operational constraints.  In the event that a WSP or WCLEC submits an application for a third or subsequent HNI, the IMSI administrator shall consult with CRTC staff before making an assignment decision.

### 8.0	RESPONSIBILITIES OF HNI APPLICANTS AND ASSIGNEES

HNI applicants and assignees shall comply with the following:

  - HNI applicants and assignees must meet all conditions specified in these Guidelines.  Copies of these Guidelines may be accessed from the CNA’s website at:  www.cnac.ca.

  - HNI applicants shall submit their requests to the IMSI administrator using Form A - Home Network Identity (HNI) Application.  Copies of all required forms are included in Attachment 1 to these Guidelines.

  - HNI assignees shall:

8.3.1	Assign and efficiently manage the MSINs (last nine digits of the IMSI) associated with the assigned HNI, and maintain MSIN assignment records.  Reports from these records may be required for audit purposes.

8.3.2	Inform the IMSI administrator of changes to the information associated with an HNI assignment by using Form D – Request for Change in Home Network Identity (HNI) Assignment Information.  Changes may occur because of the transfer of an HNI, through merger or acquisition, to a different wireless network.  The initial assignee of the HNI involved in a transfer occurring through merger, acquisition or other means must immediately inform the IMSI administrator when such a change becomes effective.  Timely submission of change information enables the IMSI administrator to maintain accurate HNI assignment records.

    - Participate in an IMSI audit process, when requested by the appropriate regulatory authority.

    - Deploy any HNI, either assigned directly by the IMSI administrator or obtained through merger or acquisition, within the specified time period, from the date of initial assignment (Section 6.10).  Inform the IMSI administrator of HNI deployment by submitting Form C – Home Network Identity (HNI) Deployment.

    - Apply to the IMSI administrator for an extension, in accordance with these Guidelines if the HNI is not deployed within the specified time period from the date of initial assignment, and the HNI is still required.

    - Return to the IMSI administrator, using Form F – Home Network Identity (HNI) Assignment Return,

- Any HNI no longer needed for the provision of WSP or WCLEC services authorized by the appropriate Canadian regulatory authority.

- Any HNI not deployed within the time period specified, including extensions.

- Any HNI not used in conformance with these Guidelines.

### 9.0	RESPONSIBILITIES OF THE IMSI ADMINISTRATOR

The IMSI administrator shall:

  - Provide general and specific information to the industry on the structure and proper use and management of IMSIs for WSPs and WCLECs.

  - Provide copies of these Guidelines and forms to HNI applicants and assignees, and assist them in completing the required forms.

  - Review and process HNI applications as follows:

    - Review the application to determine if all requested information is provided and credible.  If not, return the application to the applicant requesting that any deficiency be corrected.

    - Inform applicants of the status of their requests using Form B – Home Network Identity (HNI) Application Disposition.  There are three possible dispositions:  approved, denied, or additional information required.  Notify the applicant in writing of the disposition within 14 calendar days from receipt of Form A.  The response will include:

- If assigned, the specific HNI(s) assigned,

- If denied, the reasons for denial and instructions on how and where to appeal the decision,

- If additional information is required, the specific information required.

  - Use the following assignment procedures:

    - The administrator shall generally assign HNIs in numerical sequence by MCC and by MNC within each MCC.  The next MCC in numerical sequence should not be used until all MNCs in the preceding MCC have been assigned.

    - There may be technical consideration or limitations on the part of the licensee that require a specific assignment or preclude them being able to use the next consecutive MNC assignment.  These exceptions are set forth below and in the addendum to this document.

Accommodation for backward compatibility for existing mobile networks only identified by 10-digit mobile identification numbers (MINs):  The following HNIs are not available for assignment in order to support inter-networking with wireless network licensees requiring backward compatibility for existing mobile networks only identified by 10-digit MINs:

302-000 through 302-009

    - HNI applicants eligible for multiple MNCs may request that such MNCs be assigned in the next available block of numerically sequential codes (excepting those MNCs reserved or unavailable for assignment, in accordance with these Guidelines or any subsequent addenda to these Guidelines).  In such cases, a separate Form A should be submitted for each MNC required, along with a cover letter requesting their assignment in a sequential block.

    - A returned or reclaimed HNI should be reassigned prior to the assignment of any HNI from a MCC of higher numerical value than the returned or reclaimed HNI.  When assigning an HNI that has been reclaimed or returned, the administrator will ensure that the HNI has remained dormant for the required period.

  - Maintain accurate and current HNI assignment records.  Update the records as required to respond to requests for changes in assignment information reported by HNI assignees.  Respond to these requests within 14 calendar days using Form E - Confirmation of Change of Home Network Identity (HNI) Assignment Information.

  - Publish and maintain on the CNA’s website (www.cnac.ca), a list of assigned HNIs.  The list will include the HNI number and the wireless network licensee’s organization name.  The IMSI administrator shall track the number of HNIs assigned and the assignment rate and advise the CSCN when action needs to be taken to expand the available resource.  When the CSCN determines that additional resources are required, the IMSI administrator should also inform CRTC staff, the ITU National Study Group 2 Chair and Industry Canada.

  - Investigate any HNI that has not been deployed within the required time frame, and issue extensions if appropriate.

  - Reclaim assigned HNIs , in accordance with these Guidelines.

  - Direct the IMSI conservation program and conduct periodic audits of HNI assignee records, as required.

### 10.0	HNI RETURN AND RECLAMATION PROCEDURES

  - Assignee responsibilities:

Assignees will return HNIs that are no longer required, not deployed, or not used in conformance with these Guidelines.

Assignees will cooperate with the IMSI administrator in carrying out its reclamation and auditing responsibilities.

  - Administrator responsibilities:

The IMSI administrator will contact any HNI assignee identified as not having returned to the administrator, for reassignment, any HNI no longer required, not deployed, or not used in conformance with these Guidelines.

The administrator will first seek clarification from the assignee regarding any alleged non-use or misuse.  If the assignee provides an explanation satisfactory to the administrator, and in conformance with these Guidelines, the HNI will remain assigned.  If no satisfactory explanation is provided, the administrator will request a Form F from the assignee returning the assigned HNI for reassignment.  If a direct contact cannot be made with the assignee to affect the above process, a registered letter will be sent to the assignee’s address of record requesting that they contact the administrator within thirty days regarding the alleged HNI non-use or misuse.  If the letter is returned as non-delivered, the administrator will advise the CRTC that the HNI will be made available for reassignment following the required dormant period, if any, unless the CRTC advises otherwise.

The IMSI administrator will:

- Accept all referrals of alleged non-use or misuse of HNIs, and investigate and review such referrals in the context of these Guidelines.

- Attempt to resolve the referral or, if appropriate, initiate the Guidelines revisions process and or refer the case to the CRTC.

### 11.0	IMSI RESOURCE CONSERVATION AND ASSIGNMENT AUDITS

  - Assignment and management of Canadian IMSI resources are undertaken with the following conservation objectives:

- To efficiently and effectively administer/manage a limited resource through code conservation, and

- To eliminate or delay the exhaust potential for the MCCs currently assigned to Canada.

  - To promote the efficient and effective use of numbering resources, audits of HNI assignments may be performed to ensure consistent compliance with these Guidelines.

### 12.0	MCC RELIEF PLANNING

  - When 70% of the HNIs for a given MCC have been assigned, the IMSI administrator will inform the CSCN, CRTC staff and the ITU Study Group 2 Chair that MCCs assigned to Canada are approaching exhaust.

  - When the IMSI administrator informs the CSCN, CRTC staff and the ITU Study Group 2 Chair that the MCCs assigned to Canada are approaching exhaust, the IMSI administrator will:

- Conduct an audit of current IMSI assignment reports to determine if IMSI utilization is efficient and, if necessary,

- Provide the requisite data to CRTC staff and the ITU Study Group 2 Chair and request additional MCC resources from the ITU-T.

- Currently, MCCs 303-307 are not allocated.  Should additional MCCs be required by Canada, MCCs in this list of unallocated MCCs could be requested in order to continue with consecutive MCC allocations.

### 13.0	MAINTENANCE OF GUIDELINES

It may be necessary to modify these Guidelines periodically to meet changing and unforeseen circumstances.  The need for Guidelines modification may be identified by the administrator, the CRTC or any entity in the wireless telecommunications sector.  The CSCN will coordinate the modification process.  Questions or concerns regarding the maintenance of the Guidelines may be directed to the Canadian Numbering Administrator, 60 Queen Street, Suite 1516, Ottawa, Ontario  K1P 5Y7 (Telephone:  613-563-7242).

### 14.0	APPEALS PROCESS

Disagreements may arise between the IMSI administrator and HNI applicants or assignees in the context of the administration and management of IMSIs and the application of these Guidelines. In all cases, the IMSI administrator and HNI applicants/assignees will make reasonable, good faith efforts to resolve such disagreements among themselves, consistent with these Guidelines, prior to pursuing any appeal. Appeals may include, but are not limited to, one or more of the following options:

- The HNI applicant/assignee will have the opportunity to resubmit the matter to the administrator for reconsideration with or without additional input.

- The HNI applicant/assignee submits an appeal to the CRTC to change the IMSI administrator’s action.

Reports on any resolution resulting from the above options, the content of which will be mutually agreed upon by the involved parties, will be kept on file by the administrator. At minimum, the report will contain the final disposition of the appeal; e.g. whether or not an HNI was assigned.

### 15.0	GLOSSARY

Canadian Numbering Administrator (CNA) – The entity responsible for the administration of Canadian numbering resources, including IMSIs.

Canadian Radio-television and Telecommunications Commission (CRTC) – The CRTC is the Canadian regulatory body for broadcasting and telecommunications.  Its responsibilities include the regulation and administration of domestic numbering.

Canadian Steering Committee on Numbering (CSCN) – The CSCN is a subtending working group of the CISC.

Conservation - Consideration given to the efficient and effective use of a finite resource in order to minimize the cost and need to expand its availability while at the same time allowing the maximum flexibility in the introduction of new services, capabilities and features.

CRTC Interconnection Steering Committee (CISC) – The CISC is an organization established by the CRTC to assist in developing information, procedures, and guidelines that may be required in various aspects of the CRTC’s regulatory activities.

Home Network Identity (HNI) – The HNI uniquely identifies the home wireless network of a WSP or WCLEC subscriber and contains the Mobile Country Code (MCC) and the Mobile Network Code (MNC).  The IMSI administrator administers only the HNI segment of the IMSI.  The HNI contains the MCC followed by the MNC and is a fixed 6-digit length.

HNI assignee - The entity to which an HNI has been assigned for the provision of WSP or WCLEC service.

Home wireless network - The network authorized by Industry Canada to which the mobile station is subscribed.

International Mobile Station Identity (IMSI) - The mobile station identifier uniquely identifying the mobile station nationally and internationally. The IMSI may be associated with a subscription.  The IMSI provides a uniform and unique home wireless network and station identification that is recognizable by all conforming wireless networks, domestically and internationally.  When transmitted between visited and home wireless networks, the IMSI enables the exchange of subscription and billing information for the visiting mobile station.

International Telecommunication Union (ITU) - The United Nations Specialized Agency in the field of telecommunications.

ITU Telecommunication Standardization Sector (ITU-T) – The ITU-T is a permanent organ of the ITU.  The ITU-T is responsible for studying technical, operating and tariff questions and issuing Recommendations on them with a view to standardizing telecommunications on a worldwide basis.

Mobile Country Code (MCC) – The function of the MCC is to identify the domiciliary country of a mobile station.  By analyzing the MCC, a foreign visited wireless network can determine the country from which the mobile station originated and in which its home wireless network resides.

Mobile Network Code (MNC) – The function of the MNC is to identify the home wireless network, within the country associated with the MCC, of the visiting mobile station.  The visited wireless network uses the MCC-MNC combination to identify and query the home wireless network of the visiting mobile station that is requesting service.

Mobile station - Interface equipment used to terminate the radio path at the user side.  As noted in Recommendation E.212, the mobile station includes both card operated mobile stations and mobile stations that are not card operated.  In a card operated station, the IMSI may be contained in the card. In stations which are not card operated, the IMSI is contained in the physical mobile station.

Mobile Station Identification Number (MSIN) – The MSIN is directly administered by the wireless network licensee to which the HNI is assigned.  The function of the MSIN is to uniquely identify a mobile station within its home wireless network.

National Mobile Station Identity (NMSI) – The NMSI contains the MNC followed by the MSIN and is, therefore, a fixed twelve-digit length in Canada.  It is the national portion of the IMSI (i.e., excluding the MCC).

Visited wireless network - The network from which the mobile station obtains service.

Wireless Service Provider (WSP) or Wireless Competitive Local Exchange Carrier (WCLEC). - A Canadian entity authorized by Industry Canada pursuant to the Radiocommunication Act to provide two-way common carrier wireless mobility communications service to the public.  Examples of WSPs or WCLECs include cellular, Personal Communications Services (PCS), Enhanced Specialized Mobile Radio (ESMR), and Mobile Satellite Services (MSS).

### APPENDIX 1 - Temporary Accommodation for GSM-Based Wireless Networks

Currently GSM-based wireless networks can handle only 2-digit MNCs. This limitation can be accommodated until such time as GSM-based wireless networks will be modified to support 3-digit MNCs through the following temporary Guideline:

- MNCs in the format XX0, where X equals any of the decimal digits 0 through 9, are reserved for assignment to WSPs and WCLECs choosing to deploy "GSM-based" technology. When a licensee meeting this requirement requests code assignment, the next such code in numerical sequence will be assigned. Such codes from the next consecutive MCC should not be assigned until all such codes from the preceding MCC have been assigned.

- Until July 1, 1998, MNCs in the format XX1 through XX9 may not be assigned to WSPs and WCLECs choosing to deploy “GSM-based” technology.

INTERNATIONAL MOBILE STATION IDENTITY (IMSI)

APPLICATION AND RELATED FORMS PACKAGE

The forms in this package are used for communication between the IMSI administrator and applicants for and assignees of these resources. Forms included in this package are:

Form A - Home Network Identity (HNI) Application

Applicants complete, sign, and return this form to apply for an HNI.

Form B - Home Network Identity (HNI) Application Disposition

The administrator uses this form to notify the applicant of the outcome of his/her application, which may be a code assignment, denial, or a request for additional clarifying information.

Form C - Home Network Identity (HNI) Deployment

The recipient of an HNI assignment uses this form to notify the administrator that the assigned code has been deployed.

Form D - Request for Change in Home Network Identity (HNI) Assignment Information

HNI assignees use this form to notify the administrator of a change in any of the assignment information; for example, a change in the name, address, or phone number of the contact person in the company holding the HNI. As a more complex example, this form should also be used to record the transfer of an HNI to a new company, as might happen as a result of a merger or acquisition.

Form E - Confirmation of Change of Home Network Identity (HNI) Assignment Information

The administrator uses this form to acknowledge a change initiated by a HNI assignee through submission of Form D.

Form F – Home Network Identity (HNI) Assignment Return

HNI assignees use this form to return to the pool any HNIs which are no longer required.

Return completed forms to the administrator.

Canadian Numbering Administrator

60 Queen St., Suite 1516

Ottawa, Ontario  K1P 5Y7

Tel:  613-563-7242

Fax:  613-563-9293

E-mail:  glenn.pilley@cnac.ca

FORM A - HOME NETWORK IDENTITY (HNI) APPLICATION

Entity requesting assignment:......................................................................................................….

OCN:………………………………………………………………………………………………………….

General description of the service to be provided:........................................................................…

.

.

Is this a request for an additional HNI assignment?

( YES	( NO

If YES, please list the existing HNI assignment(s) and provide a description of the technical or operational constraint as well as an explanation of how the assignment of an additional HNI will resolve the technological or operational constraint (if required, please provide the information via an attachment):

.

.

(The application continues on the reverse side of this page.)

FORM A - HOME NETWORK IDENTITY (HNI) APPLICATION

(CONTINUED)

Contact name: ..............................................................................................................................

Company: ..................................................................................................................................…

Address: .....................................................................................................................................…

City, Province, Postal Code: ...........................................................................................................

Phone: 	  Fax: 	  E-mail: ………………………..

Signature below indicates that the applicant:

  - Certifies the accuracy of the information provided in this application,

  - Commits to deploy any assigned HNI(s) within the time period specified by the assignment guidelines,

  - Certifies that the service to be provided with the HNI is a WSP or WCLEC service, or conforms with other authorized uses as outlined in E.212,

  - Certifies that any required authorization has been secured from Industry Canada and/or the CRTC, and

  - Understands and agrees that the use of any assigned HNI(s) in a manner other than in conformance with these Guidelines may result in forfeiture.

If you have not provided the IMSI Administrator with copies of the appropriate regulatory authorization in accordance with either the Radiocommunication Act or the Telecommunications Act, then copies of such authorization must be attached to this application.

Authorized name: .......................................................................................................................

Authorized signature: ..............................................................................................................…

Date of application: .....................................................................................................................

Return completed application forms to the IMSI administrator:

Canadian Numbering Administrator

60 Queen St., Suite 1516

Ottawa, Ontario  K1P 5Y7

Tel:  613-563-7242

Fax:  613-563-9293

E-mail:  glenn.pilley@cnac.ca

FORM B - HOME NETWORK IDENTITY (HNI) APPLICATION DISPOSITION

Your application filed __________________________ for OCN(s) ___________________________________

for assignment of a HNI has been reviewed by the administrator. The box checked below indicates the

action taken:

____________________________________________________________________________________

(	Your application has been approved. The HNI assigned for your use is:

.		.

The assignment is effective as of: ...............................................................................

The information recorded for this assignment is shown below. Please notify the administrator immediately of any errors in or changes to this information.

____________________________________________________________________________________

(	Your application has been denied for the following reason(s):

.		.

.		.

…		.

You are entitled to appeal this denial as specified in these Guidelines.

____________________________________________________________________________________

(	The following additional information is needed to process your application:

.		.

.		.

.		.

____________________________________________________________________________________

Authorized name:  ………………………………………………………………………………………………..

Authorized signature:  ……………………………………………………………………………………………

E-mail address:  …………………………………………………………………………………………………..

Date:  ………………………………………………………………………………………………………………

FORM C - HOME NETWORK IDENTITY (HNI) DEPLOYMENT FORM

By submitting this form, I certify that

HNI: ............................................................................................................................................….

Entity Assigned to:  ...........................................................................................................................

E-mail Address:  …………………………………………………………………………………………….

OCN(s): ……………………………………………………………………………………………………...

Is deployed effective (date): ...................................................................................................……....

_______________________________________________________________________________________

Authorized name: .......................................................................................................................

Authorized signature: ................................................................................................................

E-mail address: ………………………………………………………………………………………….

Date of this notification: .............................................................................................................

_______________________________________________________________________________________

Return completed application forms to the IMSI administrator:

Canadian Numbering Administrator

60 Queen St., Suite 1516

Ottawa, Ontario  K1P 5Y7

Tel:  613-563-7242

Fax:  613-563-9293

E-mail:  glenn.pilley@cnac.ca

FORM D - REQUEST FOR CHANGE IN HOME NETWORK IDENTITY (HNI)

ASSIGNMENT INFORMATION

Effective (date): ..........................................................................................................................

The assignment information for HNI: 	should be changed.  The changes are

described below:

OCN(s):……………………………………………………………………………………………………………………..

Company Name:

Description:______________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

_______________________________________________________________________________________

Authorized name: .......................................................................................................................

Authorized signature: ................................................................................................................

E-mail Address:  ………………………………………………………………………………………..

Date of this notification: .............................................................................................................

_______________________________________________________________________________________

Return completed application forms to the IMSI administrator:

Canadian Numbering Administrator

60 Queen St., Suite 1516

Ottawa, Ontario  K1P 5Y7

Tel:  613-563-7242

Fax:  613-563-9293

E-mail:  glenn.pilley@cnac.ca

FORM E - CONFIRMATION OF CHANGE IN HOME NETWORK IDENTITY (HNI)

ASSIGNMENT INFORMATION

Company Name:  ___________________________________________________________________

OCN(s):___________________________________________________________________________

Name of Requester:__________________________________________________________________

Your request dated _________________________ for change(s) to the assignment information for HNI

_______________ has been processed by the administrator and the changes have been made. Please

verify the revised assignment information below and report any errors or discrepancies to the

administrator.

_______________________________________________________________________________________

Authorized name: .......................................................................................................................

Authorized signature: ..............................................................................................................…

E-mail address:  …………………………………………………………………………………………

Date of this notification: ...........................................................................................................…

Canadian Numbering Administrator

60 Queen St., Suite 1516

Ottawa, Ontario  K1P 5Y7

Tel:  613-563-7242

Fax:  613-563-9293

E-mail:  glenn.pilley@cnac.ca

FORM F - HOME NETWORK IDENTITY (HNI) ASSIGNMENT RETURN

HNI: .............................................................................................................................................. Currently held by: ..............................................................................OCN(s)......................................... is no longer required effective (date) ...................................................................................... and is being returned to the pool for assignment to another entity.

_______________________________________________________________________________________

Authorized name: .......................................................................................................................

Authorized signature: ..............................................................................................................…

E-mail Address:  …………………………………………………………………………………………

Date of this notification: ...........................................................................................................…

Return completed forms to the IMSI administrator:

Canadian Numbering Administrator

60 Queen St., Suite 1516

Ottawa, Ontario  K1P 5Y7

Tel:  613-563-7242

Fax:  613-563-9293

E-mail:  glenn.pilley@cnac.ca

# Text boxes

Mobile Country

Code (MCC)

3-digits

Mobile Network

Code (MNC)

3-digits

Mobile Station Identification

Number (MSIN)

9-digits

International Mobile Station Identity

(IMSI)

National Mobile Station Identity (NMSI)

Home Network Identity (HNI)